## Slide 1: Chapter 3
Decoding on a bus system

## Slide 2: Partial & full address decoding

## Slide 3: Signals on a RAM
RAMs typically contain several memory locations
To read/write to a particular location, an address must be provided and decoded
Memory decoding is necessary
This takes place within the RAM
6116
(2k RAM)
Address Bus
Data Bus
A10
Control Bus
Notes: In contrast to the processor address bus, the memory address bus will tell a memory device​
which particular location is being accessed. The number of memory address lines required​
depends on the size of the memory device. (e.g. a device with 1 K (i.e. 1 0 2 4) locations,​
requires 10 address lines, because 2 to the power of ten equals 1 0 2 4).​
​
In the same way, the quantity of data stored at each memory location depends on the particular​
memory device. It may be a single bit, or 4, 8 or 16 bits per location. Units of memory may be​
connected in parallel to meet the processor data width. For example, four 8 bit memory​
devices may be connected in parallel to a 32 bit processor.​
​
The block diagram of a memory device is as shown. To access data, the following steps are executed. ​
One, the address is placed on the address bus. The lower bits will be used by the memory device for​
internal decoding, the higher bits go to a decoder chip which will generate a chip select C S​
signal. This will then select one of the several memory devices. ​

## Slide 4: Accessing Memory Devices
During a memory or I/O READ cycle,
  Processor puts address on Address Bus
  Processor generates a Read Signal
  Memory or I/O Device place data on Data Bus
  Processor reads Data Bus
Notes: If we are doing a read operation, the processor will generate a read signal R D which is connected to​
the output enable O E of the memory chip. The memory device will place the data from the​
memory location after a short delay. The processor then reads in the data.​

## Slide 5
During a memory or I/O WRITE cycle,
  Processor puts address on Address Bus
  Processor puts data on Data Bus
  Processor generates a Write Signal
  Memory or I/O Device will latch the data in
Accessing Memory Devices
Notes: If we are doing a write operation, the processor will places the data to be written on the data bus, then​
The processor generates a write W R signal, which is connected to the write enable W E of the memory​
chip. The memory device will then latch the data in.​

## Slide 6: Partial and Full Address Decoding
Partial Address Decoding
CPU has 16 address lines (A0 – A15)
Some are used to address the RAM (A0 – A10)
Some are not used (A11 - A15)
This causes Memory Foldover - each location has > 1 address
A 13
E.g.
The following Addresses all access the same memory location in the RAM
0234H, 1234H and 9234H
Memory folds over 25 or 32 times
8080 Address Bus
6116
A10
A11
A15
Notes: In most practical situations, the devices connected to a processor address bus require fewer address bits than there are bits provided on the address bus. The 8080 bus has 16 pins while a 6 1 1 6 RAM has only 11 pins. Since there are 5 pins unused by the RAM chip, then this is a case of partial address decoding. This causes memory foldover where each address location has more than 1 address. If we have a memory system where all the address pins are used in memory access, we then have full address decoding.​
​
For example, the following addresses all access the same memory location in the RAM​
​
​
When a memory address or group of physical addresses respond to several different​
processor addresses, the effect is known as memory fold over. In the example above, there is a​
32 times fold over.​
​
​

## Slide 7
Decoder
CS
Full Address Decoding:
In full decoding, all CPU address pins are used
Pins not used by RAM are decoded externally
Output of external decoder connected to Chip Select of RAM
Each location now has a unique address
A 11
Partial and Full Address Decoding
8080 Address Bus
A10
A15
6116

## Slide 8: Address Decoding
Most systems contain >1 MEMORY chip
Each chip must occupy a different address range within the memory map
Each chip will have some addressing pins to select their internal locations
They will require an external circuit that will select the chip itself
This is called “address decoding circuit”.

## Slide 9: Tools for Decoding

## Slide 10: The 74LS138 3-8 Decoder
3 Chip Select Pins
3 Input Pins
To enable Decoder,
G1 = 1
G2A = G2B = 0
3 pins, 8 combinations
Only 1 pin active at any one time
8 output Pins
Notes: When connecting several memory ICs to an address bus, we can use logic gates as address​
decoders using K-Maps or standard Boolean logic. However, it is much easier to use​
demultiplexers or decoders, because of the way memory is laid out, which in many cases is in​
sequential blocks of addresses.​
​
One of the most commonly used demultiplexers is the 7 4 1 3 8 1-of-8 demultiplexer., or a 3 line to 8 line dmultiplexer

## Slide 11: 74LS138 Truth Table
INPUTS |  |  |  |  |  | OUTPUTS |  |  |  |  |  |  | 
ENABLE |  |  | SELECT |  |  |  |  |  |  |  |  |  | 
G2B | G2A | G1 | C | B | A | Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7
X | X | L | X | X | X | H | H | H | H | H | H | H | H
X | H | X | X | X | X | H | H | H | H | H | H | H | H
H | X | X | X | X | X | H | H | H | H | H | H | H | H
L | L | H | L | L | L | L | H | H | H | H | H | H | H
L | L | H | L | L | H | H | L | H | H | H | H | H | H
L | L | H | L | H | L | H | H | L | H | H | H | H | H
L | L | H | L | H | H | H | H | H | L | H | H | H | H
L | L | H | H | L | L | H | H | H | H | L | H | H | H
L | L | H | H | L | H | H | H | H | H | H | L | H | H
L | L | H | H | H | L | H | H | H | H | H | H | L | H
L | L | H | H | H | H | H | H | H | H | H | H | H | L
Notes: This slide show the truth table of the 74138.​
We will not discussed the entries highlighted in red.​
As shown in the previous slide, in order to enable the decoder, the chip select pins, G2A and G2B will be low and G1 will be high​
Looking at the output pins, note that the pin that goes low will correspond to the binary input at pins A, B and C. ​
​
We see that the 74138 can select one of eight possible devices based on its ABC inputs. If we add​
this to the eleven inputs of the 6 1 1 6, we see that we now have fourteen (11 plus 3) inputs, which still causes foldover.

## Slide 12: Comparator: 74LS85
Enable
Notes: To take care of this, we can still choose to use logic gates, but we introduce another device, the​
7 4 L S 8 5 bit comparator which may be rather overspecified for the task at hand, but it is versatile.​
​
We use only the A=B output. ​
The output will go high when A inputs equal B inputs and IA=B (or pin 3) is held high. The truth table is shown in the next slide.​
​
We can set the desired bit pattern at either the A or B inputs.​
​
Another important point is that there are other devices connected to the system that use up certain parts of the memory map. Thus we need flexibility in locating the starting address of our memory block

## Slide 13: Comparator: 74LS85
Notes: From the truth table of the 74LS85 , we see that when the digital value at the A inputs equal the digital value at the B inputs, then the A=B pin will go high when IA=IB is high.​

## Slide 14: A Design Example:
Design a 16K memory space starting from 8000H, using 6116 memory chips.
Notes: In designing a full decoding system using a 7 4 1 3 8, we should note the number of address lines that are used by the memory chip itself. This is because these lines cannot be used for decoding. Thus only the remaining lines on the host processor address bus is available. ​
​
To summarize, we may use the following steps:​
1) Identify how many address pins the memory chip uses.​
2) Calculate the number of chips that are required in the design.​
3) Draw the memory map of the design. Do this by laying out the chips contiguously, that is,​
the starting address of a chip follows immediately after the last address of the previous​
chip. Write down the range of addresses of each chip in hexadecimal.​
4) Draw a truth table. This is the binary representation of the range of addresses.​
5) Looking at the bits, observe any pattern of numbers, for example, running binary numbers​
in the bits.​
6) Fit this pattern to the truth table of the 7 4 1 3 8. First, see which address pins are to be​
assigned to inputs A, B and C. Then see how to assign the remaining address pins to the​
Enable inputs of the 7 4 1 3 8.​
7) If there are unassigned processor address pins, assign them to the 7 4 6 8 8.​
Finally, produce the schematic.

## Slide 15: Step 1
The memory device used is 6116
This is an 2048 bytes by 8 bit device
It uses address pins A0 to A10 (211 = 2048)
Each chip will take up 204810 or 7FFH address space
Notes: Now, in greater detail:​
1) The memory device to be used is a 6 1 1 6, which is a 2 0 4 8 by 8 bit device. This device uses 11 address pins A 0 to A 10. (2 to the power of 11 = 2 0 4 8). Each chip will take up 2 0 4 8 or 7 F F H addresses.​

## Slide 16: Step 2
Since we require 16K bytes in the design, we need eight 6116 chips (16K/2K)
Start Address is 8000H
RAM 1 ‑ 8000H to 87FFH
RAM 2 ‑ 8800H to 8FFFH
RAM 3 ‑ 9000H to 97FFH
RAM 4 ‑ 9800H to 9FFFH
RAM 5 ‑ A000H to A7FFH
RAM 6 ‑ A800H to AFFFH
RAM 7 ‑ B000H to B7FFH
RAM 8 ‑ B800H to BFFFH
Notes: 2) Since we require 16 K bytes in the design, we need 8 chips. (16 K over 2 K).
3) This 16 K will occupy the range from hexadecimal 8 0 0 0 to B F F F . So the first memory chip will start from 8 0 0 0 0 and occupy the address range 8 0 0 0 0 to 8 7 F F. We continue until we get the following memory map:

## Slide 17: Step 2 – continued
Start Address is 8000H
RAM 1 ‑ 8000H to 87FFH
Convert range to binary
1000 0000 0000 0000 (8000H)
1000 0111 1111 1111 (87FFH)
Replace changing bits by X
A15 A11 A10 A0
1 0 0 0 0 X--------X. 80000 - 87FFH
Notes: To draw the truth table, let us look at the first chip. It occupies the address range hexadecimal 8 0 0 0 to 8 7 F F. We can convert this range to binary, and note that the MSB is address line A15, as shown in the slide.​
​
We are not interested in the address lines used by the chip at this point. Note that the 0's and 1's​
change only at lines A 0 to A 10. ​
​
Now in order to simplify the design process, we will introduce a notation. Instead of writing two lines with all the 0's and 1's, we will represent the above range by Xs.​
​
X means that the value for the address line can be 0 or 1. The dashed line x dash dash dash x means that address lines from A 0 to A 10 can be 0 or 1. So they are not available for general use. This highlights the fact that only address lines A 15 to A 11 are available for decoding. Proceeding in similar fashion for the other chips, we have the following truth table.​
​

## Slide 18: Step 2 – continued
A15 A14 A13 A12 A11 A10-- - - - - - - - - - A0
1 0 0 0 0 x-----------------------x 8000-87FFH
1 0 0 0 1 x-----------------------x 8800-8FFFH
1 0 0 1 0 x-----------------------x 9000-97FFH
1 0 0 1 1 x-----------------------x 9800-9FFFH
1 0 1 0 0 x-----------------------x A000-A7FFH
1 0 1 0 1 x-----------------------x A800-AFFFH
1 0 1 1 0 x-----------------------x B000-B7FFH
1 0 1 1 1 x-----------------------x B800-BFFFH
Much neater, can observe patterns in the bits easily

## Slide 19: Step 3: Truth table
A15 A14 (For Full decoding) | A13 A12 A11 (chip selection) | A10 ……………A0 (Location select inside chip)
1 0 (8000H) | 0 0 0 | 0 0 0 ---------- 0
1 0 (87FFH) | 0 0 0 (Y0) | 1 1 1 ----------- 1
1 0 (8800H) | 0 0 1 | 0 0 0 ----------- 0
1 0 (8FFFH) | 0 0 1 (Y1) | 1 1 1 ------------1
Notes: 1. Looking at the truth table, we can see the address lines A 13 to A 11 taking on values that​
increment, starting from 000 to 111. If we assign these lines to a 7 4 1 3 8, we can enable up to 8 devices one at a time, depending on the values of A 15 to A 13.​
​

## Slide 20: Step 3a:Truth table – look for pattern
Pattern of ascending bits! (can be others)
Fit on to the 74LS138 ===========
Notes: 2. Comparing this with the truth table of the 7 4 1 3 8, we see that A 13 should be assigned to​
input C, A 12 to B and A 11 to A. Note that this incrementing bit pattern is only true for this​
situation. Other situations will have different patterns at different address lines. The important thing is to look out for a pattern to fit to the truth table of the 7 4 1 3 8.​
​

## Slide 21: Step 3b:Truth table – remaining bits
All bits same - 74LS688 will activate when bits appear on address bus
Set once
DIP switch
When address bus data matches
the DIP switch settings, pin 6 will
Go high!
High
Notes: 3. It is convenient to let A 15 to A 14 be enabled by the 7 4 L S 8 5, so when A 15 to A 14 has the hexadecimal value 2 and when the B inputs also has the same value, the output of the 74LS85 goes high. The B inputs values can be set by using dip switches

## Slide 22: Step 4: Circuit
Notes: This slide shows the completed circuit. Here, we use the 7485 to check if A14 and A15 is equal to the B inputs to the device. When they are the same, the output will go high and enable the next device, which is the 74138. Then depending on the binary value of A11, A12 and A13, the associated memory chip will be enabled.​

## Slide 23: Trying out the circuit – click for animation
Let’s test the circuit out – e.g. 9400 is output on address bus
1001 0100 0000 0000
CPU o/p on address lines A15-14 – 10
Bit pattern 10 is set on B inputs
The A=Bo pin will go high
CPU o/p on address lines A13-11 – 010
This sets CS2 to low
RAM3 selected and location 9400H accessed in chip
Notes: Lets try our circuit. ​
Lets say the hexadecimal value 9400 is output onto the address bus.​
We convert 9400 to binary.​
Bit 15 and 14 is sent to the A inputs of the 7485. ​
These corresponds to the B inputs whose values are set by switches.​
Since A inputs is the same as B inputs, the output goes high and in turn enable the 74138.​
Depending on the values of A11, A12 and A13 which are 0, 1 and 0 respectively, this will make the corresponding output pin goes low, in this case CS2.​
Which in turn will enable the corresponding memory device.

## Slide 24: Input/Output Decoding
We consider using buffers and latches for interfacing to input/output devices
Buffer or latch needs 1 address only
Decode each device exactly
Notes: As we saw before, memory devices use only some of the available address lines. The lower address lines will select a single memory location in the memory device. The higher address lines from the system are used by a decoder to select one of several memory devices. Also, the memory device will have an Output Enable pin for a read and a RAM device will also have a Write Enable pin.​
​
Now, We consider using buffers and latches for interfacing to input/output devices. Buffers and latches have only a single address location so we need to decode each device exactly.

## Slide 25: Example
Design an input port of address 30H and an output port of address 31H
Truth Table
A5 A4 A3 A2 A1 A0
1 1 0 0 0 1 31H (output port)
1 1 0 0 0 0 30H (input port)
(To be constrained (C B A of 74138)
by 74LS85)
Notes: Lets look at an example to design an input port of address 30 hex and an output port of address 31 hex​
The truth table shows the breakdown of the addresses in binary

## Slide 26
Input Device
(Buffer)
Output Device (Latch)
Notes: We let A 0-A 2 be decoded by the 7 4 1 3 8. The bit pattern on the ‘B’ inputs correspond to bits A 3- A 5.
As we see, the 7 4 L S 8 5 in conjunction with a 7 4 1 3 8 allows us to decode individual I/O addresses.
The 7 4 8 5 activates a block of 8 devices through the 7 4 1 3 8. The starting address of this block will have the A 0 to A 2 pins at logic 0. This address is known as the base address as all the other I O addresses are simply added to the base to get its address.

## Slide 27: Summary of Input/Output Decoding
Selecting memory chip enables device only
  Internal decoder selects memory location
Buffers/latches need full decoding
Control signals for memory have a dedicated pin
Buffers latches may need extra logic gate for this
Notes: Memory devices contain many storage locations within itself. Selecting a memory chip through a decoder only enables the chip. Internal decoding circuitry within the memory chip will select individual memory locations.
Buffers and latches, being individual devices, need full decoding to be done externally as it does not have the circuitry internally.
In addition to enable pins, memory devices have control pins which determine whether data is written or read to.
Buffers and latches are normally activated through a single control pin. Again, external gates may be needed to correctly decode the signal.

## Slide 28: Chapter 3